## Slide 1
RHODA
Virtual Lab Assistant for R&S Oscilloscopes
Track 2: Virtual Lab Assistant (Conversational / Voice)
Rohde & Schwarz AI-Assisted Onboarding Hackathon Kwame Nkrumah University of Science and Technology June 2026
Team: Afari · Gregory · William · Prince

## Slide 2
THE PROBLEM
New students struggle with oscilloscope procedures
→ Novices lack accessible step-by-step guidance
→ Translating lab procedures into commands is error-prone
→ Safety mistakes risk equipment damage and injury
→ No feedback on what went wrong or why
→ Instructors can't track individual student progress
What students need:
• A guide that speaks their language
• Step-by-step walkthrough of procedures
• Safety checks before touching hardware
• Real-time instrument feedback
• Adaptive learning that tracks progress

## Slide 3
OUR SOLUTION
Rhoda — conversational AI lab assistant
Voice + Text Chat Interface
Ask questions naturally, get step-by-step guidance
Safety-Gated Instrument Control
Every WRITE command requires explicit confirmation
AI-Powered Troubleshooting
Describe a bad trace → get diagnosis + fix steps
XR Avatar (Quest Headset)
3D assistant with lip sync and hand tracking
Real R&S RTB24 Integration
SCPI control via RsInstrument over USB
Guided Workflows
2 demo flows: measurement + safety procedures
RAG Knowledge Base
15 documents from RTB2 manual + procedures
Progress Tracking
9 competency areas, curriculum-ordered learning

## Slide 4
SYSTEM ARCHITECTURE
FRONTEND (TypeScript + Vite)
XR Avatar — Three.js + WebXR + IWSDK
Text Chat — /chat.html lab console
Instructor — /instructor.html dashboard
Voice — Gemini STT/TTS + GhanaNLP (Twi)
RAG — 18 embedded procedure/safety docs
Anomaly — fault pattern matching + Gemini
BACKEND (Flask + Python)
13 REST API endpoints
RAG retrieval (sentence-transformers)
Instrument API with confirmation gate
Session logging + progress tracking
Failure point analytics
TECHNOLOGY STACK
Three.js + WebXR 3D rendering, XR
Meta IWSDK hand tracking, panels
Google Gemini 2.5 LLM, vision, STT, TTS
GhanaNLP API Twi speech + translation
Flask 3.0 REST backend
sentence-transformers RAG embeddings
RsInstrument R&S VISA/SCPI driver
METRICS
6,720 lines of code
22 TypeScript + 6 Python modules
15 RAG corpus documents
45 GLB animation assets
11 automated backend tests
13 API endpoints
3 web entry points

## Slide 5
DEMO WORKFLOW 1: SIMPLE
Measure a 1 kHz Sine Wave (10 steps)
1. Connect probe to CH1 BNC input
2. Set probe attenuation to 10X
3. Enable CH1
4. Set vertical scale to 1 V/div
5. Set timebase to 500 µs/div
6. Set trigger: CH1, rising edge, auto
7. Adjust trigger level to midpoint
8. Verify waveform is stable
9. Read measurement (expect ~1 kHz)
10. Review results
Each instrument-changing step triggers a confirmation prompt. The student must approve before the oscilloscope setting changes.

## Slide 6
DEMO WORKFLOW 2: SAFETY-CRITICAL
Handle an Overvoltage Warning (6 steps)
⚠ Step 1: STOP — Disconnect probe from the circuit immediately
Overvoltage can damage the instrument and create a safety hazard
⚠ Step 2: Check signal voltage with a multimeter before reconnecting
⚠ Step 3: Verify voltage is within safe limits (300V CAT II with 10X probe)
Step 4: Select correct probe attenuation (10X or 100X for high voltage)
Step 5: Set oscilloscope to maximum V/div range before reconnecting
Step 6: Reconnect probe carefully, verify no overload warning

## Slide 7
SAFETY ARCHITECTURE
Every instrument change requires explicit approval
Confirmation Gate
1. User or Rhoda requests a change
2. Backend generates preview with:
• Current value
• Proposed value
• Human-readable summary
• Unique confirmation token
3. Student sees prompt and decides
4. Only confirmed changes execute
5. Token expires if state changes
Safety Rules
• READ operations never need confirmation
• WRITE operations always need confirmation
• Parameter safety limits enforced
(V/div: 1mV–10V, timebase: 1ns–50s)
• Overvoltage detection → immediate warning
• Default to simulator mode
• Real hardware only with SCOPE_RESOURCE
• No PII in session logs
• Anomaly detection flags unsafe traces

## Slide 8
REAL HARDWARE: R&S RTB24
SCPI commands verified against RTB2 User Manual
Connection (via RsInstrument Python library):
pip install RsInstrument pyvisa-py
SCOPE_RESOURCE=USB python server/app.py
Verified SCPI commands:
CHANnel<m>:STATe ON|OFF
CHANnel<m>:SCALe <V/div>
CHANnel<m>:COUPling DCLimit|ACLimit|GND
TIMebase:SCALe <s/div>
TRIGger:A:SOURce CH1..CH4
TRIGger:A:LEVel1:VALue <volts>
TRIGger:A:EDGE:SLOPe POSitive|NEGative
MEASurement<m>:MAIN FREQuency|PEAK|RMS
MEASurement<m>:RESult:ACTual?
Data flow:
Chat / Voice
↓
Flask Backend (:5001)
↓
Confirmation Gate (preview → approve)
↓
RsInstrumentBackend
↓
SCPI over USB TMC
↓
R&S RTB24 Oscilloscope
Auto-discovery: list_resources('?*')
Fallback: simulator if hardware unavailable

## Slide 9
TRACK 2 DELIVERABLES
All requirements met
✓ Live demo: 2 guided workflows (simple + safety-critical)
✓ Assistant guides user step-by-step through procedures
✓ Instrument configuration after explicit confirmation
✓ Voice interaction (Gemini STT/TTS + GhanaNLP Twi)
✓ Text chat interface (/chat.html)
✓ Conversation transcripts (export JSON + server API)
✓ Instructor view of logs and failure points
✓ README with instrument/simulator connection guide
✓ Code repository on GitHub
Stretch goals achieved:
✓ Voice integration with lip-synced avatar
✓ Auto-configure instruments after confirmation
✓ Twi language support (GhanaNLP)
✓ AR component identification (Gemini Vision)
✓ Anomaly detection with safety flags
✓ Competency-based progress tracking

## Slide 10
TEAM
Four cores, one assistant
Afari
Stream I/O
Mic/camera capture, STT/TTS pipeline, avatar lip-sync, audio recorder
Gregory
RAG / Context
15-document corpus, procedure/safety/fault knowledge base, sentence-transformer retrieval
William
Instrument API
R&S RTB24 SCPI control, confirmation gate, RsInstrument integration, USB auto-discovery
Prince
Vision / Logging
Component ID (Gemini Vision), anomaly detection, session logging, competency tracking, progress system

## Slide 11
Thank You
Rhoda — Virtual Lab Assistant
github.com/PhidLarkson/rohde-schwarz-assistant
Demo: /chat.html · XR Avatar · /instructor.html Backend: python server/app.py | SCOPE_RESOURCE=USB for real hardware